## Slide 1: Instruction Set of 8086 Microprocessor

## Slide 2: Instruction set basics
Instruction:- An instruction is a binary pattern designed inside a microprocessor to perform a specific function.
Opcode:-
  It stands for operational code.
  It specifies the type of operation to be performed by CPU.
  It is the first field in the machine language instruction format.
  E.g. 08 is the opcode for instruction “MOV X,Y”.
Operand:-
  We can also say it as data on which operation should act.
  Operands may be register values or memory values.
  The CPU executes the instructions using information present in this field. It may be 8-bit data or 16-bit data.

## Slide 3: Instruction set basics
Assembler:- it converts the instruction into sequence of binary bits, so that this bits can be read by the processor.
Mnemonics:- these are the symbolic codes for either instructions or commands to perform a particular function.
  E.g. MOV, ADD, SUB etc.

## Slide 4: Assignment of codes to Registers

## Slide 5: Types of instruction set of 8086 microprocessor
(1). Data Copy/Transfer instructions.
(2). Arithemetic & Logical instructions.
(3). Branch instructions.
(4). Loop instructions.
(5). Machine Control instructions.
(6). Flag Manipulation instructions.
(7). Shift & Rotate instructions.
(8). String instructions.

## Slide 6: (1). Data copy/transfer instructions.
(1). MOV Destination, Source;
There will be transfer of data from source to destination.
Source can be register, memory location or immediate data.
Destination can be register or memory operand.
Both Source and Destination cannot be memory location or segment registers at the same time.
E.g.
(1). MOV CX, 037A H;
(2). MOV AL, BL;
(3). MOV BX, [0301 H];

## Slide 7
BX | 2000H
AX | 2000H
BEFORE EXECUTION
AFTER EXECUTION
MOV BX,AX;
AH |  | AL | 
BH |  | BL | 
CH |  | CL | 
DH |  | DL | 
AH |  | AL | 
BH |  | BL | 
CH |  | CL | 40
DH |  | DL | 
MOV CL,M;
40
40
BEFORE EXECUTION
AFTER EXECUTION

## Slide 8: Stack Pointer
It is a 16-bit register, contains the address of the data item currently on top of the stack.
Stack operation includes pushing (providing) data on to the stack and popping (taking)data from the stack.
Pushing operation decrements stack pointer and Popping operation increments stack pointer. i.e. there is a last in first out (LIFO) operation.

## Slide 9: (1). Data copy/transfer instructions.
(2). Push Source;
Source can be register, segment register or memory.
This instruction pushes the contents of specified source on to the stack.
In this stack pointer is decremented by 2.
The higher byte data is pushed first (SP-1).
Then lower byte data is pushed (SP-2).
E.g.:
(1). PUSH AX;
(2). PUSH DS;
(3). PUSH [5000H];

## Slide 10
INITIAL POSITION
DECREMENTS SP & STORES HIGHER BYTE
HIGHER BYTE
DECREMENTS SP & STORES LOWER BYTE
LOWER BYTE
HIGHER BYTE
(1) STACK POINTER
(2) STACK POINTER
(3) STACK POINTER

## Slide 11
BH |  | BL | 
CH | 10 | CL | 50
DH |  | DL | 
BH |  | BL | 
CH | 10 | CL | 50
DH |  | DL | 
50
10
SP | 2002H
SP | 2000H
BEFORE EXECUTION
AFTER EXECUTION
2000H
2001H
2002H
2000H
2001H
2002H
PUSH CX

## Slide 12: (1). Data copy/transfer instructions.
(3). POP Destination;
Destination can be register, segment register or memory.
This instruction pops (takes) the contents of specified destination.
In this stack pointer is incremented by 2.
The lower byte data is popped first (SP+1).
Then higher byte data is popped (SP+2).
E.g.
(1). POP AX;
(2). POP DS;
(3). POP [5000H];

## Slide 13
INITIAL POSITION AND READS LOWER BYTE
LOWER BYTE
INCREMENTS SP & READS HIGHER BYTE
LOWER BYTE
HIGHER BYTE
INCREMENTS SP
LOWER BYTE
HIGHER BYTE
(1) STACK POINTER
(2) STACK POINTER
(3) STACK POINTER

## Slide 14
BH |  | BL | 
BH | 50 | BL | 30
SP | 2000H
SP | 2002H
30
50
30
50
BEFORE EXECUTION
AFTER EXECUTION
POP BX
2000H
2001H
2002H
2000H
2001H
2002H

## Slide 15: (1). Data copy/transfer instructions.
(4). XCHG Destination, source;
This instruction exchanges contents of Source with destination.
It cannot exchange two memory locations directly.
The contents of AL are exchanged with BL.
The contents of AH are exchanged with BH.
E.g.
(1). XCHG BX, AX;
(2). XCHG [5000H],AX;

## Slide 16
AH | 20 | AL | 40
BH | 70 | BL | 80
AH | 70 | AL | 80
BH | 20 | BL | 40
BEFORE EXECUTION
AFTER EXECUTION
XCHG AX,BX;

## Slide 17: (1). Data copy/transfer instructions.
(5). IN AL/AX, 8-bit/16-bit port address
It reads from the specified port address.
It copies data to accumulator from a port with 8-bit or 16-bit address.
DX is the only register is allowed to carry port address.
E.g.
(1). IN AL, 80H;
(2). IN AX,DX; //DX contains address of 16-bit port.

## Slide 18
 | 10
AL | 
 | 10
AL | 10
BEFORE EXECUTION
AFTER EXECUTION
IN AL,80H;
PORT 80H
PORT 80H

## Slide 19: (1). Data copy/transfer instructions.
(6). OUT 8-bit/16-bit port address, AL/AX;
It writes to the specified port address.
It copies contents of accumulator to the port with 8-bit or 16-bit address.
DX is the only register is allowed to carry port address.
E.g.
(1). OUT 80H,AL;
(2). OUT DX,AX; //DX contains address of 16-bit port.

## Slide 20
 | 10
AL | 40
 | 40
AL | 40
BEFORE EXECUTION
AFTER EXECUTION
OUT 50H,AL;
PORT 50H
PORT 50H

## Slide 21: (1). Data copy/transfer instructions.
(7). XLAT;
Also known as translate instruction.
It is used to find out codes in case of code conversion.
i.e. it translates code of the key pressed to the corresponding 7-segment code.
After execution this instruction contents of AL register always gets replaced.
E.g. XLAT;
Mnemonic | Meaning | Format | Operation | Flags
XLAT | Translate | XLAT | ((AL)+(BX)+(DS)0)  (AL) | None

## Slide 22: (1). Data copy/transfer instructions.
Mnemonic | Meaning | Format | Operation | Flags affected
LEA | Load Effective Address | LEA Reg16,EA | EA  (Reg16) | None
LDS | Load Register And DS | LDS Reg16,MEM32 | (MEM32)  (Reg16) (Mem32+2)  (DS) | None
LES | Load Register and ES | LES Reg16,MEM32 | (MEM32)  (Reg16) (Mem32+2)  (DS) | None

## Slide 23: (1). Data copy/transfer instructions.
(8). LEA 16-bit register (source), address (dest.);
LEA Also known as Load Effective Address (LEA).
It loads effective address formed by the destination into the source register.
E.g.
(1). LEA BX,Address;
(2). LEA SI,Address[BX];

## Slide 24: (1). Data copy/transfer instructions.
(9). LDS 16-bit register (source), address (dest.);
(10). LES 16-bit register (source), address (dest.);
LDS Also known as Load Data Segment (LDS).
LES Also known as Load Extra Segment (LES).
It loads the contents of DS (Data Segment) or ES (Extra Segment) & contents of the destination to the contents of source register.
E.g.
(1). LDS BX,5000H;
(2). LES BX,5000H;

## Slide 25
10
20
30
40
5000H
5001H
5002H
5003H
20 | 10
40 | 30
(1). LDS BX,5000H;
(2). LES BX,5000H;
BX
DS/ES
0
7
0
15

## Slide 26: (1). Data copy/transfer instructions.
(11). LAHF:- This instruction loads the AH register from the contents of lower byte of the flag register.
This command is used to observe the status of the all conditional flags of flag register.
E.g. LAHF;
(12). SAHF:- This instruction sets or resets all conditional flags of flag register with respect to the corresponding bit positions.
If bit position in AH is 1 then related flag is set otherwise flag will be reset.
E.g. SAHF;

## Slide 27: (1). Data copy/transfer instructions.
(13). PUSH F:- This instruction decrements the stack pointer by 2.
It copies contents of flag register to the memory location pointed by stack pointer.
E.g. PUSH F;
(14). POP F:- This instruction increments the stack pointer by 2.
It copies contents of memory location pointed by stack pointer to the flag register.
E.g. POP F;

## Slide 28: (2). Arithematic Instructions
These instructions perform the operations like:
Addition,
Subtraction,
Increment,
Decrement.

## Slide 29: (2). Arithematic Instructions
(1). ADD destination, source;
This instruction adds the contents of source operand with the contents of destination operand.
The source may be immediate data, memory location or register.
The destination may be memory location or register.
The result is stored in destination operand.
AX is the default destination register.
E.g. (1). ADD AX,2020H;
(2). ADD AX,BX;

## Slide 30
AH | 10 | AL | 10
AFTER EXECUTION
BEFORE EXECUTION
AH | 10 | AL | 10
BH | 20 | BL | 20
AFTER EXECUTION
BEFORE EXECUTION
ADD AX,2020H
ADD AX,BX
2050
AH | 30 | AL | 30
1010
+2020
3030
AH | 30 | AL | 30
BH | 20 | BL | 20

## Slide 31: (2). Arithematic Instructions
(2). ADC destination, source
This instruction adds the contents of source operand with the contents of destination operand with carry flag bit.
The source may be immediate data, memory location or register.
The destination may be memory location or register.
The result is stored in destination operand.
AX is the default destination register.
E.g. (1). ADC AX,2020H;
(2). ADC AX,BX;

## Slide 32
AH | 10 | AL | 10
AFTER EXECUTION
BEFORE EXECUTION
AH | 10 | AL | 10
BH | 20 | BL | 20
AFTER EXECUTION
BEFORE EXECUTION
ADC AX,2020H
ADC AX,BX
2050
AH | 30 | AL | 31
1010
+2020
3030+1=3031
AH | 30 | AL | 31
BH | 20 | BL | 20
CY | 1
CY | 1

## Slide 33: (2). Arithematic Instructions
(3). INC source
This instruction increases the contents of source operand by 1.
The source may be memory location or register.
The source can not be immediate data.
The result is stored in the same place.
E.g. (1). INC AX;
(2). INC [5000H];

## Slide 34
AFTER EXECUTION
5000H
AFTER EXECUTION
BEFORE EXECUTION
INC [5000H]
BEFORE EXECUTION
INC AX
AH | 10 | AL | 10
AH | 10 | AL | 11
1010
5000H
1011

## Slide 35: (2). Arithematic Instructions
(4). DEC source;
This instruction decreases the contents of source operand by 1.
The source may be memory location or register.
The source can not be immediate data.
The result is stored in the same place.
E.g. (1). DEC AX;
(2). DEC [5000H];

## Slide 36
AFTER EXECUTION
5000H
AFTER EXECUTION
BEFORE EXECUTION
DEC [5000H]
BEFORE EXECUTION
DEC AX
AH | 10 | AL | 10
AH | 10 | AL | 0F
1010
5000H
100F

## Slide 37: (2). Arithematic Instructions
(5). SUB destination, source;
This instruction subtracts the contents of source operand from contents of destination.
The source may be immediate data, memory location or register.
The destination may be memory location or register.
The result is stored in the destination place.
E.g. (1). SUB AX,1000H;
(2). SUB AX,BX;

## Slide 38
AFTER EXECUTION
BEFORE EXECUTION
SUB AX,1000H
AFTER EXECUTION
BEFORE EXECUTION
SUB AX,BX
AH | 20 | AL | 00
AH | 10 | AL | 00
2000
-1000
=1000
AH | 20 | AL | 00
BH | 10 | BL | 00
AH | 10 | AL | 00
BH | 10 | BL | 00

## Slide 39: (2). Arithematic Instructions
(6). SBB destination, source;
Also known as Subtract with Borrow.
This instruction subtracts the contents of source operand & borrow from contents of destination operand.
The source may be immediate data, memory location or register.
The destination may be memory location or register.
The result is stored in the destination place.
E.g. (1). SBB AX,1000H;
(2). SBB AX,BX;

## Slide 40
AH | 20 | AL | 20
AFTER EXECUTION
BEFORE EXECUTION
AH | 20 | AL | 20
BH | 10 | BL | 10
AFTER EXECUTION
BEFORE EXECUTION
SBB AX,1000H
SBB AX,BX
2050
AH | 10 | AL | 19
2020
- 1000
1020-1=1019
AH | 10 | AL | 19
BH | 10 | BL | 10
B | 1
B | 1

## Slide 41: (2). Arithematic Instructions
(7). CMP destination, source
Also known as Compare.
This instruction compares the contents of source operand with the contents of destination operands.
The source may be immediate data, memory location or register.
The destination may be memory location or register.
Then resulting carry & zero flag will be set or reset.
E.g. (1). CMP AX,1000H;
(2). CMP AX,BX;

## Slide 42
AFTER EXECUTION
CMP AX,BX
BEFORE EXECUTION
CY | 0 | Z | 1
AFTER EXECUTION
BEFORE EXECUTION
D=S: CY=0,Z=1
D>S: CY=0,Z=0
D<S: CY=1,Z=0
AH | 10 | AL | 00
BH | 10 | BL | 00
CMP AX,BX
CY | 0 | Z | 0
AH | 10 | AL | 00
BH | 00 | BL | 10
AFTER EXECUTION
BEFORE EXECUTION
CMP AX,BXH
CY | 1 | Z | 0
AH | 10 | AL | 00
BH | 20 | BL | 00

## Slide 43: (2). Arithematic Instructions
(8). AAA
Also known as ASCII Adjust After Addition.
This instruction is executed after ADD instruction.
(1). IF lower bits of AL<=09 then,
Higher bits of AL should loaded with zeroes.
There should be no change in lower bits of AL.
AH also must be cleared (AH=0000 0000).
(2). IF lower bits of AL>09 then,
Bits of AL must be incremented by 06 (i.e. AL+0110).
Bits of AH must be incremented by 01 (i.e. AH+0001).
Then higher bits of AL should be loaded with 0000.
E.g. (1). AAA;

## Slide 44
6 | 7
0 | 7
6 | A
0 | 0
BEFORE EXECUTION
BEFORE EXECUTION
AFTER EXECUTION
AFTER EXECUTION
(1). FOR AL<=09H
AL
AL
(1). FOR AL>09H
AL
AL
(A)1010 +(06)0110=0001 0000
HB
LB
Hb
Lb
Hb
Lb
Hb
Lb
Hb
Lb
Hb=Higher bits,
Lb=Lower bits.

## Slide 45: (2). Arithematic Instructions
(9). AAS
Also known as ASCII Adjust After Subtraction.
This instruction is executed after SUB instruction.
(1). IF lower bits of AL<=09 then,
Higher bits of AL should loaded with zeroes.
There should be no change in lower bits of AL.
AH also must be cleared (AH=0000 0000).
(2). IF lower bits of AL>09 then,
Bits of AL must be decremented by 06 (i.e. AL-0110).
Bits of AH must be decremented by 01 (i.e. AH-0001).
Then higher bits of AL should be loaded with 0000.
E.g. (1). AAS;

## Slide 46
6 | 7
0 | 7
6 | A
0 | 4
BEFORE EXECUTION
BEFORE EXECUTION
AFTER EXECUTION
AFTER EXECUTION
(1). FOR AL<=09H
AL
AL
(1). FOR AL>09H
AL
AL
(A)1010 -(06)0110=0000 0100
Hb
Lb
Hb
Lb
Hb
Lb
Hb
Lb
Hb
Lb
Hb=Higher bits,
Lb=Lower bits.

## Slide 47: (2). Arithematic Instructions
(10). AAM
Also known as ASCII Adjust After Multiplication.
This instruction is executed after MUL instruction.
Then AH=AL/10 & AL=Remainder.
E.g. MOV AL,04 // AL=04
MOV BL,09 // BL=09
MUL BL // 04*09=36 (i.e. BL*AL)
AAM // AH=03 & AL=06
E.g. (1). AAM;

## Slide 48: (2). Arithematic Instructions
(11). AAD;
Also known as ASCII Adjust before Division.
Then AL=AH*10 +AL & AH=0.
E.g. MOV AX, 0105 // AH=01, AL=05
AAD // AL=15 (i.e.0FH) & AH=00
E.g. (1). AAD;

## Slide 49: (2). Arithematic Instructions
(12). DAA;
Decimal Adjust Accumulator.
IF lower bits of AL>09.
Then AL=AL+06.
E.g. MOV AL,53H //AL=53H
MOV CL,29H //CL=29H
ADD AL,CL // AL=7CH (i.e. 12=C) & C>9.
DAA // AL=7C+06=82H. (i.e. 0111 1100 + 0000 0110)=1000 0010
E.g. (1). DAA;
7
C
0
6
+
8 2
=

## Slide 50: (2). Arithematic Instructions
(13). DAS
Decimal Adjust after Subtraction.
IF lower bits of AL>09.
Then AL=AL-06.
E.g. MOV AL,30H // AL=30H
MOV CL,20H // CL=20H
SUB AL,CL // AL=0AH (i.e. A=10) & C=10>9.
DAS // AL=0A-06=04H. (i.e. 0000 1010 - 0000 0110)=0000 0100
E.g. (1). DAS;
0
A
0
6
-
0 4
=

## Slide 51: (2). Arithematic Instructions
(14). MUL operand
Unsigned Multiplication.
Operand contents are positively signed.
Operand may be general purpose register or memory location.
Result is stored in accumulator (AX).
when operand is a byte:
  AX = AL * operand.
when operand is a word:
  (DX AX) = AX * operand.
E.g. (1). MUL BH // AX= AL*BH; // (+3) * (+4) = +12.
(2). MUL CX // AX=AX*CX;

## Slide 52: (2). Arithematic Instructions
(15). IMUL operand
Signed Multiplication.
Operand contents are negatively signed.
Operand may be general purpose register, memory location or index register.
If operand is of 8-bit then multiply it with contents of AL.
If operand is of 16-bit then multiply it with contents of AX.
Result is stored in accumulator (AX).
E.g. (1). IMUL BH // AX= AL*BH; // (-3) * (-4) = 12.
(2). IMUL CX // AX=AX*CX;

## Slide 53: (2). Arithematic Instructions
(16). DIV operand
Unsigned Division.
Operand may be register or memory.
Operand contents are positively signed.
Operand may be general purpose register or memory location.
AL=AX/Operand (8-bit/16-bit) & AH=Remainder.
E.g. MOV AX, 0203 // AX=0203
MOV BL, 04 // BL=04
DIV BL // AX=0203/04=80 (i.e. AL=50 & AH=00)

## Slide 54: (2). Arithematic Instructions
(17). IDIV operand
Signed Division.
Operand may be register or memory.
Operand contents are negatively signed.
Operand may be general purpose register or memory location.
when operand is a byte:
  AL = AX / operand
  AH = remainder (modulus)
when operand is a word:
  AX = (DX AX) / operand
  DX = remainder (modulus)
E.g. MOV AX, -0203 // AX=-0203
MOV BL, 04 // BL=04
DIV BL // AL=-0203/04=-50 (i.e. AL=-80 & AH=00)

## Slide 55: (3). Logical Instructions
(1). AND destination, source
Destination operand may be register, memory location.
Source operand may be register, immediate data or memory location.
Result is stored in destination operand.
E.g. MOV AX, 3F0FH // AX=3F0FH
MOV BX, 0008H // BX=0008H
AND AX,BX // AX=0008H

## Slide 56
Follow the rules as given below:-
(1). 1 AND 1 = 1
(2). 1 AND 0 = 0
(3). 0 AND 1 = 0
(4). 0 AND 0 = 0
3F0FH= 0011 1111 0000 1111
0008H=0000 0000 0000 1000
0000 0000 0000 1000 = 0008H

## Slide 57: (3). Logical Instructions
(2). OR destination,source
Destination operand may be register, memory location.
Source operand may be register, immediate data or memory location.
Result is stored in destination operand.
E.g. MOV AX, 3F0FH // AX=3F0FH
MOV BX, 0098H // BX=0098H
OR AX,BX // AX=3F9FH

## Slide 58
Follow the rules as given below:-
(1). 1 OR 1 = 1
(2). 1 OR 0 = 1
(3). 0 OR 1 = 1
(4). 0 OR 0 = 0
3F0FH= 0011 1111 0000 1111
0098H=0000 0000 1001 1000
0011 1111 1001 1111 = 3F9FH

## Slide 59: (3). Logical Instructions
(3). NOT operand;
Operand may be register, memory location.
This instruction inverts (complements) the contents of given operand.
Result is stored in Accumulator (AX).
E.g. MOV AX, 0200FH // AX=200FH
NOT AX // AX=DFF0H

## Slide 60
Follow the rules as given below:-
(1). 1 NOT = 0
(2). 0 NOT = 1
200FH= 0010 0000 0000 1111
1101 1111 1111 0000 = DFF0H

## Slide 61: (3). Logical Instructions
(4). TEST destination,source
Both operands may be register, memory location or immediate data.
This instruction performs bit by bit logical AND operation for flags only (i.e. only flags will be affected).
If the corresponding 0th bit of result contains ‘1’ then result will be non-zero & zero flag will be cleared/reset (i.e. ZF=0).
If the corresponding 0th bit of result contains ‘0’ then result will be zero & zero flag will be set (i.e. ZF=1)..
E.g. (1). TEST AX,BX
(2). TEST [0500],06H

## Slide 62: (3). Logical Instructions
(5). Shift and Rotate Instructions
SHL/SAL: shift logical left/shift arithmetic left
SHR: shift logical right
SAR: shift arithmetic right
ROL: rotate left
ROR: rotate right
RCL: rotate left through carry
RCR: rotate right through carry

## Slide 63: SHL Instruction
The SHL (shift left) instruction performs a logical left shift on the destination operand, filling the lowest bit with 0.
Operand types:
SHL reg,imm8
SHL mem,imm8
SHL reg,CL
SHL mem,CL

## Slide 64: Fast Multiplication
Shifting left 1 bit multiplies a number by 2
Shifting left n bits multiplies the operand by 2n
  For example, 5 * 22 = 20
mov dl,5
shl dl,1
mov dl,5
shl dl,2 ; DL = 20

## Slide 65
Ex.; Multiply AX by 10
      SHL AX, 1
      MOV BX, AX
      MOV CL,2
      SHL AX,CL
      ADD AX, BX

## Slide 66: SHR Instruction
The SHR (shift right) instruction performs a logical right shift on the destination operand. The highest bit position is filled with a zero.
Shifting right n bits divides the operand by 2n
MOV DL,80
SHR DL,1 ; DL = 40
SHR DL,2 ; DL = 10

## Slide 67: SAR Instruction
SAR (shift arithmetic right) performs a right arithmetic shift on the destination operand.
An arithmetic shift preserves the number's sign.
MOV DL,-80
SAR DL,1 ; DL = -40
SAR DL,2 ; DL = -10

## Slide 68: (3). Logical Instructions
RCR
Also known as Rotate Right through Carry.
Each binary bit of the operand is rotated towards right by one position through Carry flag.
Least Significant Bit (LSB) i.e. B0 is placed in the Carry flag.
Then carry flag bit is placed in the Most Significant Bit (MSB) position B15.

## Slide 69
B0 | B0 | B0 | B1 | B0 | B0 | B0 | B1
AFTER EXECUTION
BEFORE EXECUTION
B1 | B1 | B0 | B1 | B0 | B0 | B1 | B0
CF
0
B0 | B0 | B0 | B0 | B1 | B0 | B 0 | B0
B0 | B1 | B1 | B0 | B1 | B0 | B0 | B1
CF
1
15
0
0
15
7
7

## Slide 70: (3). Logical Instructions
(6). RCL
Also known as Rotate Left through Carry.
Each binary bit of the operand is rotated towards left by one position through Carry flag.
Least Significant Bit (LSB) of operand i.e. B0 is placed in the B1.
Then Most Significant Bit (MSB) of operand is placed in carry flag bit.

## Slide 71
AFTER EXECUTION
BEFORE EXECUTION
B0 | B0 | B0 | B1 | B0 | B0 | B0 | B1
B1 | B0 | B0 | B1 | B0 | B0 | B1 | B0
CF
0
B0 | B0 | B1 | B0 | B0 | B0 | B1 | B0
B0 | B0 | B1 | B0 | B0 | B1 | B0 | B0
CF
1

## Slide 72: ROL Instruction
ROL (rotate) shifts each bit to the left
The highest bit is copied into both the Carry flag and into the lowest bit
No bits are lost
MOV Al,11110000b
ROL Al,1 ; AL = 11100001b
MOV Dl,3Fh
ROL Dl,4 ; DL = F3h

## Slide 73: ROR Instruction
ROR (rotate right) shifts each bit to the right
The lowest bit is copied into both the Carry flag and into the highest bit
No bits are lost
MOV AL,11110000b
ROR AL,1 ; AL = 01111000b
MOV DL,3Fh
ROR DL,4 ; DL = F3h

## Slide 74: String?
An array of bytes or words located in memory
Supported String Operations
  Copy (move, load)
  Search (scan)
  Store
  Compare

## Slide 75: String Instruction Basics
Source DS:SI, Destination ES:DI
  You must ensure DS and ES are correct
  You must ensure SI and DI are offsets into DS and ES respectively
Direction Flag (0 = Up, 1 = Down)
  CLD - Increment addresses (left to right)
  STD - Decrement addresses (right to left)

## Slide 76: String Instructions
Instruction prefixes
Prefix | Used with | Meaning
REP REPE/REPZ REPNE/REPNZ | MOVS STOS CMPS SCAS CMPS SCAS | Repeat while not end of string CX ≠ 0 Repeat while not end of string and strings are equal. CX ≠ 0 and ZF = 1 Repeat while not end of string and strings are not equal. CX ≠ 0 and ZF = 0

## Slide 77: Instructions
Mnemo- Nic | meaning | format | Operation | Flags effect-ed
MOVS | Move string DS:SI ES:DI | MOVSB/MOVSW | ((ES)0+(DI))  ((DS)0+(SI)) (SI)  (SI) ± 1 or 2 (DI)  (DI) ± 1 or 2 | none
CMPS | Compare string DS:SI ES:DI | CMPSB/ CMPSW | Set flags as per ((DS)0+(SI)) - ((ES)0+(DI)) (SI)  (SI) ± 1 or 2 (DI)  (DI) ± 1 or 2 | All status flags

## Slide 78
Mnemo- Nic | meaning | format | Operation
SCAS | Scan string AX – ES:DI | SCASB/ SCASW | Set flags as per (AL or AX) - ((ES)0+(DI)) (DI)  (DI) ± 1 or 2
LODS | Load string DS:SI  AX | LODSB/ LODSW | (AL or AX)  ((DS)0+(SI)) (SI)  (SI) ± 1 or 2
STOS | Store string ES:DI  AX | STOSB/ STOSW | ((ES)0+(DI))  (AL or A) ± 1 or 2 (DI)  (DI) ± 1 or 2

## Slide 79: (4). String Manipulation Instructions
(1). REP
Also known as Repeat instruction prefix.
This instruction executed repeatedly until the ‘CX’ register becomes zero.
When ‘CX’ becomes zero then program control passes to next instruction.
There are following sub types of ‘REP’ instruction,
(i). REPE:- REPeat instruction while Equal.
(ii). REPZ:- REPeat instruction while Zero.
(iii). REPNE:- REPeat instruction while Not Equal.
(iv). REPNZ:- REPeat instruction while Not Zero.

## Slide 80: (4). String Manipulation Instructions
(2). CMPS
Also known as Compare String Byte or String Word.
The length of the string must be stored in register CX.
If both the byte or word are equal then zero flag will be set (i.e. ZF=1) otherwise it will be reset (i.e. ZF=0).
When zero flag will be set then ‘CX’=0.
There are following sub types,
(i). CMPSB:- Compare String Byte.
(ii). CMPSW:- Compare String Word.

## Slide 81: (5). Branching Instructions
(1). CALL
Also known as unconditional call.
Under unconditional call, the execution control is transferred to the specified location independent of any status or condition.
This instruction is used to call subroutine from a main program.
There are following sub types,
(i). NEAR CALL:- It pushes only IP into the stack.
(ii). FAR CALL:- It pushes IP & CS into the stack.

## Slide 82: (5). Branching Instructions
(2). JMP
Also known as unconditional jump.
Under unconditional jump, the execution control is transferred to the specified location using 8-bit or 16-bit displacement.
There are following three formats of jump instruction,
(i). JMP
(ii). JMP
(iii). JMP
8-bit Displacement
IP (LB) | IP (UB) | CS (LB) | CS (UB)
16-bit Displacement (LB) | 8-bit Displacement (UB)

## Slide 83
Conditional Jump instructions
Conditional Jump instructions in 8086 are just 2 bytes long. 1-byte opcode followed by 1-byte signed displacement (range of –128 to +127). | 
Conditional Jump Instructions | 
Jumps based on a single flag | Jumps based on more than one flag

## Slide 84: Conditional Jump Instructions
Mnemonic : Jcc
Meaning : Conditional Jump
Format : Jcc operand
Operation : If condition is true jump to the address specified by operand. Otherwise the next instruction is executed.
Flags affected : None

## Slide 85
Mnemonic | meaning | condition
JA | Above | CF=0 and ZF=0
JB | Above or Equal | CF=0
JB | Below | CF=1
JBE | Below or Equal | CF=1 or ZF=1
JC | Carry | CF=1
JCXZ | CX register is Zero | (CF or ZF)=0
JE | Equal | ZF=1
JG | Greater | ZF=0 and SF=OF
JGE | Greater or Equal | SF=OF
JL | Less | (SF XOR OF) = 1
TYPES

## Slide 86
Mnemonic | meaning | condition
JLE | Less or Equal | ((SF XOR OF) or ZF) = 1
JNA | Not Above | CF =1 or Zf=1
JNAE | Not Above nor Equal | CF = 1
JNB | Not Below | CF = 0
JNBE | Not Below nor Equal | CF = 0 and ZF = 0
JNC | Not Carry | CF = 0
JNE | Not Equal | ZF = 0
JNG | Not Greater | ((SF XOR OF) or ZF)=1
JNGE | Not Greater nor Equal | (SF XOR OF) = 1
JNL | Not Less | SF = OF

## Slide 87
Mnemonic | meaning | condition
JNLE | Not Less nor Equal | ZF = 0 and SF = OF
JNO | Not Overflow | OF = 0
JNP | Not Parity | PF = 0
JNZ | Not Zero | ZF = 0
JNS | Not Sign | SF = 0
JO | Overflow | OF = 1
JP | Parity | PF = 1
JPE | Parity Even | PF = 1
JPO | Parity Odd | PF = 0
JS | Sign | SF = 1
JZ | Zero | ZF = 1

## Slide 88
Jumps Based on a single flag
JZ | r8 | ;Jump if zero flag set to 1 (Jump if result is zero)
JNZ | r8 | ;Jump if Not Zero (Z flag = 0 i.e. result is nonzero)
JS | r8 | ;Jump if Sign flag set to 1 (result is negative)
JNS | r8 | ;Jump if Not Sign (result is positive)
JC | r8 | ;Jump if Carry flag set to 1
JNC | r8 | ;Jump if No Carry
JP | r8 | ;Jump if Parity flag set to 1 (Parity is even)
JNP | r8 | ;Jump if No Parity (Parity is odd)
JO | r8 | ;Jump if Overflow flag set to 1 (result is wrong)
JNO | r8 | ;Jump if No Overflow (result is correct)
There is no jump based on AC flag

## Slide 89
JZ r8 ; JE (Jump if Equal) also means same.
JNZ r8 ; JNE (Jump if Not Equal) also means same.
JC r8 ;JB (Jump if below) and JNAE (Jump if Not Above or Equal) also mean same.
JNC r8 ;JAE (Jump if Above or Equal) and JNB (Jump if Not Above) also mean same.
JZ, JNZ, JC and JNC used after arithmetic operation
JE, JNE, JB, JNAE, JAE and JNB are used after a compare operation.
JP r8 ; JPE (Jump if Parity Even) also means same.
JNP r8 ; JPO (Jump if Parity Odd) also means same.

## Slide 90: (6). Flag Manipulation Instructions
(1). CMC
Also known as Complement Carry Flag.
It inverts contents of carry flag.
if CF = 1 then CF will be = 0.
if CF = 0 then CF will be = 1.
E.g. CMC

## Slide 91: (6). Flag Manipulation Instructions
(2). STC
Also known as Set Carry Flag.
It makes carry flag in set condition.
After execution CF = 1.
E.g. STC

## Slide 92: (6). Flag Manipulation Instructions
(3). CLI
Also known as Clear Interrupt Flag.
It makes interrupt flag in reset condition.
After execution IF = 0.
E.g. CLI

## Slide 93: (6). Flag Manipulation Instructions
(4). CLD
Also known as Clear Direction Flag.
It makes direction flag in reset condition.
After execution DF = 0.
E.g. CLD

## Slide 94: (7). Machine Control Instructions
(1). HLT
Also known as Halt
It makes the processor to be in stable (do nothing) condition.
E.g. HLT

## Slide 95: (7). Machine Control Instructions
(2). NOP
Also known as No Operation.
It tells about further there will be no operation to be performed.
E.g. NOP